Condition Monitoring of Electrolytic Capacitance in DC Power Grid

Theoretical background

During PWM=ON:

{du_0(t)} over {dt} `=` {{1} over {C}} ~cdot` {i_C(t)} (1) and i_C(t) `=`-i_0( t) `=` -{{u_0(t)} over {R_load}} (2)

During PWM=OFF:

{du_0(t)} over {dt} `=` ESR ~cdot` {di_C(t)} over {dt} ~+~ {1} over {C} ~cdot` i_C(t) (3) and i_C( t) `=` i_L(t) ~-` i_0( t) `=` i_L( t) ~-` {u_0(t)} over {R_load} (4)

Approximation to the solutions

“Estimate C”

From (1) and (2) we can get C by solving for u0(t).
{du_0(t)} over {dt} ~+` {1} over {R_load ` C} cdot u_0(t) ~=` 0
which have the analytical solution as
u_0(t) `=` u_0( 0 ) ~cdot` func e^{ -{{1} over {R_load`C}} `cdot` t }

Using Taylor series for exp(k*x) = 1 + k*x + k2*x2/2 + ... and use only first-order polynomial, we approximate the analytical solution as
u_0( t) `approx` u_0( 0 ) `cdot` left ( 1 `-` {1} over {R_load`C} `cdot t right ) or u_0( t) `approx` w_0 ~+` w_1 ~cdot`t
Once the coefficient of w0 and w1 are estimated, hence we get the capacitance from
C ~=` -{ {w_0} over {w_1`R_load} }

“Estimate ESR”

From (3) and (4), we need to solve u0(t) and iL(t) to get the ESR, provided C is known.
From signal observation, we can approximate iL(t) as first-order polynomial, while u0(t) as second-order polynomial.

{du_o(t)} over {dt} `=` ESR ~cdot` {d} over {dt} left ( i_L(t) `-` {u_o(t)} over {R_load} right ) `+` {1} over {C} `cdot` left ( i_L(t) `-` {u_o(t)} over {R_load} right )
or,
left ( 1 `+` {ESR} over {R_load} right ) ~cdot` {du_o(t)} over {dt} `+` {1} over {R_load`C} ~cdot` u_o(t)`=` ESR ~cdot` {di_L(t)} over {dt} `+` {1} over {C} ~cdot` i_L( t)
Model iL(t) as a first-order polynomial, i_L( t ) approx wi_0 `+` wi_1 ~cdot` t , hence
left ( 1 `+` {ESR} over {R_load} right ) ~cdot` {du_o(t)} over {dt} `+` { 1 } over {R_load`C} ~cdot` u_o(t) `=` ESR ~cdot` wi_1 `+` {wi_0} over {C} `+` {wi_1} over {C} ~cdot` t
Rearrange the coefficients:
{du_o(t)} over {dt} `+` {1} over {R_load`C}~cdot` { 1 } over {1`+`ESR/R_load}~cdot`u_o( t ) `=` { ESR`cdot`wi_1 ~+~ wi_0/C } over {1`+`ESR/R_load} ~+~ {wi_1/C} over {1`+`ESR/R_load}~cdot`t
The solution of differential equation for y'`+`a~cdot`y `=`b~cdot`t`+`c is
y( t )`=`- {b} over { a^{2}} ~+~ {b} over {a}~cdot`t ~+~ { c } over {a} ~+~ k~cdot` func e^{-a~cdot`t}
[source: WolframAlpha]
We get 4 coefficients while we will only use second-order polynomial (3 coefficients). Use the fact that u0(t=0)=u0(0)=v0 to eliminate 1 coefficient:
u_o( t=0 ) ~=~ v_0 ~=~ - {b} over {a^2} `+` {c} over {a} `+` k
Chose to replace c/a,
{c} over {a} `=` v_0 `+` {b} over {a^2} ~-` k , ~~rightarrow ~~ u_o( t ) `=` - {b} over {a^2} `+` {b} over {a} ~cdot`t `+` left ( v_0 `+` {b} over {a^2} `-` k right ) `+` k~cdot` func e^{-a~cdot`t}
So we can express u0(t) in 3 coefficients:
u_o( t )`=` left ( v_0 `-` k right ) `+` {b} over {a}~cdot`t ~+~ k~cdot` func e^{-a~cdot`t}
with the constants:
a ~=~ {{1} over {R_load`C}~cdot` { 1 } over {1`+`ESR/R_load}} newline b ~=~ {wi_1/C} over {1`+`ESR/R_load} newline c ~=~ { ESR`cdot`wi_1 ~+~ wi_0/C } over {1`+`ESR/R_load} ~,~ k ~=~ u_o( 0 ) `+` {b} over {a^2} `-` {c} over {a}

Since we will model u0(t) as second-order polynomial, we can approximate the exp(-a*t) using Taylor series up to second-order.
u_o( t )` approx ` left ( v_0 `-` k right ) `+` {b} over {a}~cdot`t ~+~ k~cdot` left (1 `-` a~cdot`t `+` {a^2} over {2} ~cdot`t^2 right ) ~=~ v_0 `+` left ( {b} over {a} ~-` k~cdot`a right ) ~cdot`t `+` {1} over {2} ~cdot` k ~cdot` a^2 ~cdot`t^2
Or,
u_o( t ) ` approx ` wu_0 `+` wu_1~cdot`t `+` wu_2~cdot`t^2
in which those 3 coefficients will be estimated using adaptive algorithm.

Once we get those 3 coefficients, by matching the coefficients and constans we get these system equations:
(1): wu_1 `=` {b} over {a} `-` k~cdot`a ,
(2): wu_2 `=` {1} over {2} ~cdot`k~cdot`a^2 ,
(3): a `=` {1} over {R_load`cdot`C}~cdot` {1} over {1`+`ESR/R_load} ,
(4): b `=` {wi_1/C} over {1`+`ESR/R_load} .
Combine (1) and (2) to eliminate k:
wu_1 `=` {b} over {a} `-` left ( {2~cdot`wu_2} over {a^2} right ) ~cdot`a , we get
(1+2): {b} over {a} `=` wu_1 `+` 2~cdot` {wu_2} over {a}

Combine (3) and (4) to eliminate ESR (hence to remain a and b). First modify (3) into:
a `=` {1} over {R_load`cdot`C}~cdot` {1} over {1`+`ESR/R_load} ~~ rightarrow ~~ a~cdot` left ( 1`+` {ESR} over {R_load} right ) `=` {1} over {R_load~cdot`C}
or,
ESR `=` {1} over {a~cdot`C} `-` R_load .
From (4):
b~cdot` left ( {1`+`{ESR}over{R_load}} right ) `=` wi_1 / C , then
left ( 1 `+` {1} over {R_load} ~cdot` left ( {1} over {a~cdot`C}~-` R_load right ) right ) `=` {wi_1/C} over {b} newline {1} over {a}~cdot` {1} over {R_load~cdot`C} `=` {wi_1} over {b~cdot`C} newline {b} over {a} `=` wi_1~cdot`R_load

Substitute (1+2):
{b} over {a} `=` wi_1~cdot`R_load `=` wu_1 `+` 2~cdot` {wu_2} over {a}

Hence we get a as:
a`=` {2~cdot`wu_2} over {wi_1~cdot`R_load ~-~ wu_1}
Then we can use (3) to get ESR:
ESR `=` {1} over {a~cdot`C} `-` R_load

We can also double confirm the ESR by using other equation, e.g. by evaluating b.
{b} over {a} `=` wi_1~cdot`R_load ~~ rightarrow ~ b `=` left ( {2~cdot`wu_2} over {wi_1~cdot`R_load `-` wu_1} right ) ~cdot` wi_1~cdot`R_load
b `=` {2~cdot`wu_2} over {1 `-` {1} over {R_load} ~cdot` {wu_1} over {wi_1} }
From (4):
b `=` {wi_1/C} over {1`+`ESR/R_load} ~~ rightarrow ~ ESR `=` R_load~cdot` left ( {wi_1} over {b~cdot`C} ~-` 1 right )
ESR `=` R_load~cdot` left ( {wi_1} over {{2~cdot`wu_2} over {1 `-` {1} over {R_load} ~cdot` {wu_1} over {wi_1} } ~cdot`C} ~-` 1 right ) `=` R_load~cdot` left ( {wi_1 ~cdot` left(1 `-` {1} over {R_load} ~cdot` {wu_1} over {wi_1} right)} over {2~cdot`wu_2 ~cdot`C} ~-` 1 right ) newline ESR `=` R_load ~cdot` left ( {1} over {2} ~cdot` {wi_1} over {wu_2} ~cdot` {1}over{C} ~-` {1}over{2}~cdot`{wu_1}over{wi_1}~cdot`{1}over{R_load~cdot`C} ~-` 1right )
ESR `=` {1} over {2} ~cdot` {wi_1} over {wu_2} ~cdot` {R_load}over{C} ~-` {1}over{2}~cdot`{wu_1}over{wi_1}~cdot`{1}over{C} ~-` R_load .
Somehow, prediction from a and b is not accurate. So continue to c by involving a and b.
From this result k ~=~ u_o( 0 ) `+` {b} over {a^2} `-` {c} over {a} and wu_2 `=` {1} over {2} ~cdot`k~cdot`a^2 , we get c:
c `=` left ( v_0 `+` {b} over {a^2} `-` k right ) ~cdot` a `=` left ( v_0 `+` {b} over {a^2} `-` {2~cdot`wu_2}over{a^2} right ) ~cdot` a
and the fact that v0 = wu0. Hence,
c `=` wu_0~cdot`a `+` { b }over{ a } `-` { 2~cdot`wu_2 }over{ a }
and ESR is calculated from:
c ~=~ { ESR`cdot`wi_1 ~+~ wi_0/C } over {1`+`ESR/R_load}
to get:
ESR `=` { {wi_0 }over{ C } ~-` c }over{ {c}over{R_load } ~-` wi_1 } .

In summary, to estimate the ESR:
Get all the coefficients wi0, wi1, wu0, wu1, wu2:
a`=` {2~cdot`wu_2} over {wi_1~cdot`R_load ~-~ wu_1}
b `=` {2~cdot`wu_2} over {1 `-` {1} over {R_load} ~cdot` {wu_1} over {wi_1} }
c `=` wu_0~cdot`a `+` { b }over{ a } `-` { 2~cdot`wu_2 }over{ a }
Then use them all:
ESR `=` { {wi_0 }over{ C } ~-` c }over{ {c}over{R_load } ~-` wi_1 }
Since we use all the coefficients, it yield better result than use some of the coefficients (example use “only a” or “only a and b” to estimate).